## Slide 1
Responsible Team | Haengsung Electronics company Quality Assurance team
Estimated review and update time | Max. 1 year
Author (by roll and function) | CS team member
Approver 1 | CS team member
Approver 2 | CS part leader
Revision | Date | What changed | What was removed | What was added
00 | 2026-08-17 | HSE released new standard |  | 

## Slide 2
▣ Requirement
IATF 16949 7.2.3 Competence of internal auditor 9.2 Internal Audit /9.2.1/9.2.2 9.2.2.1 Internal audit program 9.2.2.2 Quality management system audit 9.2.2.3 Process audit 9.2.2.4 Product audit
2. Customer (CSR) GM Refer to attached excel file
3. Legal/Regulatory: N/A
4. ETC: N/A (Supplier/ Interested Party)
▣ Opportunity / Risk analysis
Opportunity - Find potential issue in advanced - Improve QMS
Risk Factors Missing IATF16949 Certification Breaking up Quality Management System Cannot find out potential issue to improve QMS
Impact Cannot achieve customer requirements
Strategy - Monitoring & checking regular audit on management review - Conduct periodic training to improve internal auditor competency (including customer requirements)
▣ Resources | 
Personnel | Education : College graduation or more
 | Experience : 1 year or more
 | Training : IATF 16949 internal auditor training Internal OJT
Tools | HW: PC SW: Audit check list (VDA 6.3/ 6.5, Customer required format) Audit NCR Issue F/up sheet
Related teams | HSE All team
Team in charge | Quality Department
▣ Process Input
Past internal audit report Internal & external performance /change Risk assessment Audit Checklist Product spec, Control Plan, Work Instruction CSRs CQI 8 LPA Control Plan
System Audit Standard
▣ Process Output
Audit plan Report of audit results Non- Conforming report Corrective Action Report Internal auditor qualification list
▣ Related Processes/Standards
▣ Process step
1. Internal audit annual plan 2. Prepare details 3. Perform internal audits 4. Nonconformity reporting and corrective action follow up 5. Internal audit result report 6. Corrective action / validation 7. Maintain internal audit records 8. Internal Auditor qualification Management
▣ Performance index (KPI) |  | 
KPI | cycle | Team
Audit conduct rate | monthly | Quality

## Slide 3
Table of contents
Chapter | Content | Page
Introduction | Article 1 Scope | 07
 | Article 2 Purpose | 07
 | Article 3 Definition of terms | 07
 | Article 4 Responsibility and authority | 08
Process | Article 5 Procedure | 09
 | Article 5.1 Establishment of internal audit plan (program) and audit notice | 09
 | Article 5.2 Hold an auditor meetings and share audit related information | 10
 | Article 5.3 Perform internal audit | 12
 | Article 5.4 Non-conformity report | 12
 | Article 5.5 Report of audit result | 13
 | Article 5.6 Verify corrective action | 13
 | Article 5.7 Maintain internal audit records | 13
 | Article 5.8 Management of auditor qualification | 13
 | Article 5.9 Internal auditor qualification maintenance | 15
Epilogue | Article 6 Attachments | 15
 | Article 7 Records retention policy | 16

## Slide 4
Flow Chart
Process step | Input | Department / Team |  | Output | Approver
 |  | Quality department (planning, outgoing) | Auditee department |  | 
 | 1. Audit plan 2. Past Audit Report 3. Product Spec. 4. Control plan 5. Customer Claim list 6. Customer and External Audit Report 7. Design Change/Process Change 8. Management review 9. Shift service 10. Process information 11. Customer Specific Requirement 12. Risk assessment result |  |  |  | 
 | 1. Annual audit plan 2. Customer CSRs |  |  | Meeting minutes Checklist Audit schedule | 
 | 1. Checklist 2. Audit schedule |  |  | Nonconformity issues | 
 | 1. Nonconformity issues 2. Audit evidence Nonconformity reports |  |  | Nonconformity reports Corrective and Preventive Action plan & report | 
Prepare details
Audit annual plan
Perform audits
Nonconformity reporting and corrective action follow up
Quality Manager
Annual audit plan
Approval
Hold an auditor meetings and share audit related information
Audit notice
1
Establish an annual audit plan (program)
2
Yes
No
Perform audit
(System/manufacturing process/product)
Nonconformity reports
Request to submit corrective and preventive actions
3
4
Make & submit corrective and preventive actions plan
A

## Slide 5
Process step | Input | Responsible department | Related organizations | Output | Final approver
 |  | Quality department (planning, outgoing) | Auditee department |  | 
 | 1. Nonconformity reports 2. Corrective and Preventive Action Report |  |  |  | 
 | 1. Audit Nonconformity report 2. External audit Nonconformity report |  |  |  | 
 |  |  |  | Audit records | 
 | Internal auditor selection / training |  |  | Internal auditor qualification list Internal auditor qualification list | 
Internal Auditor qualification
Management
Corrective
action / validation
Audit result
report
Maintain audit records
A
Verify corrective action
Final audit
result report
Management of internal auditor qualification
Maintain audit records
6
8
5
7
Internal auditor qualification maintenance
9
Audit
report
Management review
Plant
Director
Quality department leader
Plant
Director

## Slide 6
INTRODUCTION
Article 1. Scope
This standard applies to all applicable departments, manufacturing processes, support processes and quality-related activities within the HSE Mexico Business Unit. The audit program includes System Audit, Process Audit, Product Audit, ESD Audit, Layered Process Audit (LPA), Control Plan & PFMEA Audit, and Special Audit, as applicable.
Article 2 Purpose
Through the systematic and independent auditing of system audits, we confirm the effectiveness and efficiency of the Haengsung Electronics company system including the quality policy and the quality assurance system, and aim to continuously improve and improve the system.
Article 3 Definition of Terms
Quality Policy: The overall intent and direction of the quality-related organization officially expressed by HSE President.
Quality Objective: To pursue or to aim for quality. Quality goals should be quantifiable.
Quality Management System: Quality Management System that directs and manages the organization. It is a system for establishing quality policy and quality goals and achieving the goals.
Quality Planning Part: Part of quality management that focuses on providing assurance that the quality requirements will be met.
System Audit: Systematic verification activities carried out on its own to determine whether the quality management system and quality assurance activities are appropriate to the intended plan, are effectively implemented, and are appropriate in achieving the organization's policies and goals.
Non-conformity: Failure to meet the prescribed requirements
1) Major Non-conformity : C grade
There is no in-house procedure to meet customer needs and expectations of CSR
requirements, or do not follow one in some requirements of procedure systematically.
2) Minor Non-conformity : B grade
There are in-house related procedures but they are not executed fully, or they run inefficiently
3) Opportunity for Improvement/ Observation : A grade
It is not a minor or significant nonconformity, but the observed situation may result
in the judge's judgment and experience not being ideal.

## Slide 7
Regular Quality Audit: It is a quality audit conducted on the overall quality system, and the Quality Department shall conduct it at least once a year for all of the departments according to the established plan.
Special Quality Audit: It is specially conducted in case that any significant change or abnormality is detected or is likely to be detected in the quality system.
Article 4 Responsibility and authority
1. Plant Director
Responsibility and authority to periodically review and determine the suitability and efficiency of the quality system to achieve quality policy and quality objectives.
2. Quality Planning Part Leader
Responsibility and authority over the overall system audit activity to assess the suitability and effectiveness of the quality system.
It has the responsibility and authority to form an audit team to conduct audits of systems, processes and products.
Responsibility and authority to plan and operate the audit.
Report the audit results to President and make them available as inputs for management review.
It establishes and inspects the audit plan for the division and has the authority to make adjustments or final decisions on the disagreement between the audit department or the auditor during the audit. Changes in plans or results should be authorized in consultation with the audit team and documented.
Monitor corrective action status.
Verification and close of corrective action as answer for Non-conformance in audits
3. Internal auditor
A planned internal audit should be carried out, and it is the responsibility of documenting and submitting the results of the audit.
The organization's quality management system, manufacturing process, and product should be reviewed to verify compliance with customer requirements and expectations or quality management system requirements, IATF16949 requirements and DILO requirements.
The quality assurance team leader should discuss with auditors about previous non-conformance, as well as other recommendations of the exchange, and make clear that the audit of the previous non conformance to the verification requirements.
Support audit team in the following and verification of corrective action as answer for Non-conformance in audits

## Slide 8
4. Auditee Department
Prepare for self-examination under the audit plan and respond to the audit requirements in good faith.
Corrective and preventive actions should be carried out on nonconformities as a result of the audit.
Report the results to the team leader in accordance with the nonconformity to confirm corrective actions and verification results.
Within the scope of the audit agreed with the audit team, the management shall be actively audited. System audits should include management reviews.
PROCESS
Article 5 Procedure
Article 5.1 Establishment of system audit plan (program) and audit notice
The audit plan shall establish the quality management system, for audits of manufacturing process and products procedure, review procedures related.
The detailed audit schedule includes the date, time, and judge assignment to identify the department, process, and product to be audited and examine each object. However, the judges (auditor) are not assigned to their departments or related process to their department . Planning is based in the risk identified in the process, result of previous audits and changes which affect the organization. Criteria for frequency of audit
The quality assurance manager may conduct system audits, even if they are not planned in the annual plan, with the approval of the president in the event of customer complaints, material changes, or audits of key customers.
The system audit plan shall be notified to the relevant department manager before the audit.
Criteria | Result | Planning
Non conformities in previous audits | 0-5 | 1 time
 | 5-10 | 2 times
 | More than 10 | 3 times
Process risk analysis | Low | 1 time
 | Medium | 2 times
 | High | 3 times

## Slide 9
5.1.1. Audit program
A) Quality management system audit
Haengsung Electronics company shall audit their own audit program named with “System Quality Audit” to encourage and improve the quality level of subsidiaries. The HQ’s audit checklist is divided into monthly audit items and conduct an audit monthly, at least report the result. The team will split the HQ’s audit items into 4 parts, this audit take 4 months to complete one-time Q-Audit. (and conduct twice a year)
For a proper following in the status of planned audits, it is a code to update every month for the planned audit in that period: P= Planned; E=Executed; R=Rescheduled; X=Not performed
B) Manufacturing process audit
In order to determine the effectiveness of the process, each manufacturing process is planned and performed as a whole or as a sample. At the time of audit, the customer-specific management plan, drawings (specifications), inspection specifications, test specifications, and process specific guidelines are reviewed. Within each individual audit plan, each manufacturing process shall be audited on all shifts where it occurs, including the appropriate sampling of the shift handover. The manufacturing process audit shall include an audit of the effective implementation of the process risk analysis (such as PFMEA), control plan, and associated documents.
C) Product audit
Internal audits are planned and carried out by selecting the appropriate stages of production and delivery (delivery) to identify the specified requirements, such as product dimensions, functions, appearance, packaging, labeling, and to verify compliance. In addition to the product, drawing by product / part, customer claim data, inspection and test specifications are reviewed.
Article 5.2. Hold an auditor meetings and share audit related information
It conducts an audit pre-meeting under the supervision of the quality department and provides the internal auditor with the audit schedule, check list, and major audit points.

## Slide 10
1) The checklist shall be prepared by the internal auditor to be used for each audit so as to conform to the audit objective using the following data:
IATF 16949 requirements
Customer-specific requirements
Quality management manuals and processes
Procedures and standards
Past customer complaints and claims reports
Design change and process change
Management plan
Past review report & checklist
Internal and external nonconforming product reports
Organizational changes and new entrants
New installation equipment and process
Newly registered subcontractors
* Table 1. Audit program requirement from each customer, and internal regulation
:Must follow customer-defined audit program,
If a customer dose not define the program, follow the regulation defined VS company-internally
Division | HSE | GM | Customer X
System audit | Quality System Audit List | - | -
Process audit | VDA 6.3 | LPA CQI | -
Product audit | VDA 6.5 | N/A | -
If applicable,
(If not applicable, follow internal program)

## Slide 11
Article 5.3 Perform audit
The auditor interviews the audit items, confirms the results of the work, confirms the documents, The examination shall be conducted on the basis of objective evidence. The audited data range is at least 6 recent months to evaluate objectively about the quality improvement tendency.
The auditor may request the auditee department to improve the nonconformity when it finds any nonconformity.
The auditor shall communicate the corrective action request to the representative of the audited department.
If the auditor is unable to conduct the audit during the scheduled audit period, or re schedule the audit in order to complete it. Information shall be handed over and carried out under the supervision of the lead auditor or the QP/CS Part Leader.
Article 5.4. Non-conformity report
5.4.1. Non-conformity report
The auditor shall fill in the nonconformity report found at the time of examination and receive confirmation from the audited department.
In the nonconformity report, evidence of nonconformity is attached as much as possible.
Quality Planning Part Leader confirms the nonconformity report and notifies the audited department in writing.
5.4.2. Corrective and preventive action
The owner of the process, where the Non-conformance was found, defines the cause using a methodology of analysis. Where the methodology is not defined previous to the analysis of cause, the 5 whys methodology would be used focused in the systemic cause, occurrence and detection can be omitted depending of nature of the case.
The audited department shall prepare a corrective and preventive action plan for nonconformities in accordance with the corrective action request, and send it to the Quality Planning Part within the require date. The required lead time for improvement is within 14 days, except long term action plan.
The audited department shall notify the Quality Planning Part of the results of the action according to the corrective and preventive action plan.

## Slide 12
Article 5.5. Report of audit result
Quality Planning Part Leader shall prepare a report on the result of the audit that includes the nonconformities of each department and report it to the top management, President and FSE in HSE.
In addition, the audit result report shall be reported at the quality meeting or management meeting for management review.
Confirm corrective action:
5.5.1) Quality Planning Part Leader makes a checklist of nonconformities in order to confirm the validity of the corrective action in the past internal audit.
5.5.2) These checklists are managed with nonconformities, including the minimum year.
Article 5.6. Verify corrective action
5.6.1) The quality department shall verify and record whether the corrective actions are being carried out effectively, and if the results of the measures are inadequate, the corrective action plan may be requested again. Time to review effectiveness, depending of the nature of countermeasure is 30, 60 and 90 days. Countermeasures related to deliver of product shall not wait this period time and shall be confirmed before the shipping date, others like following of status or revision in the process, can be monitored in this periods of time. In both cases the maintenance of corrective actions shall be verified in these 3 time intervals
5.6.2) The quality department may include previous corrective action result in the next audit program to check verification status.
Article 5.7. Maintain audit record
5.7.1) The quality assurance department is responsible for keeping all records related to the audit.
5.7.2) The retention period of the quality audit record shall be at least three years excluding the year concerned
Article 5.8. Management of auditor qualification
Haengsung Electronics company shall maintain a list of qualified internal auditors, QA-FO-19-01 Lista de auditores internos
Quality management system auditors shall be able to demonstrate the following minimum competencies:
understanding of the automotive process approach for auditing, including risk-based thinking;
understanding of applicable customer-specific requirements;
understanding of applicable ISO 9001 and IATF16949 requirements related to the scope of the audit;
understanding of applicable core tool requirements related to the scope of the audit;
understanding how to plan, conduct, report, and close out audit findings.
In case of QMS auditor, QA manager shall select qualifying auditors and initial evaluate them.

## Slide 13
Items | Need items |  | Auditor Requirements |  |  | 
 |  |  | QM System | MFG process | Product | 2nd party auditor
Training | Understanding of the automotive process approach for auditing, including risk-based thinking |  | O | O |  | O
 | Technical understanding of the relevant manufacturing process(es) to be audited, including process risk analysis (such as PFMEA) and control plan |  | O | O |  | O
 | Understanding product requirements and use of relevant measuring and test equipment to verify product conformity |  |  | O | O | 
 | Core Tool | APQP | O | O |  | O
 |  | FMEA | O | O |  | O
 |  | PPAP | O | O |  | O
 |  | Control Plan | O | O |  | O
 |  | MSA | O | O |  | O
 |  | SPC | O | O |  | O
 | ISO 9001 / IATF16949 |  | O | O |  | O
 | Audit techniques (Establishment of audit plan, execution, report writing and closing nonconformity) |  | O | O |  | O
 | Customer Specific Requirement (refer to table 1/ page 10 ) |  | O | O | O | O
 | VDA 6.3 |  |  | O |  | 
 | VDA 6.5 |  |  | O |  | 
Education | Education |  | College or higher | College or higher | High school or higher | College or higher
Experience | More than 2 year of experience in applicable field (Quality, Production, Production Engineering, Elementary, Technology, Local Development,etc) |  | O | O | O | O
Communication skill | Who can communicate for the audit (Local language, English), Interpretation permitted |  | O | O | O | O
2) Initial evaluation shall be done with the qualification Evaluation Report and members being evaluated shall have minimum score of 70 in order to be qualified
At a minimum, manufacturing process auditors shall demonstrate technical understanding of the relevant manufacturing process(es) to be audited, including process risk analysis (such as PFMEA) and control plan.
At a minimum, product auditors shall demonstrate competence in understanding product requirements and use of relevant measuring and test equipment to verify product conformity. (Manufacturing process & Product auditable organization: quality, production, production engineering, elementary technology, local development staff).

## Slide 14
Article 5.9 Internal auditor qualification maintenance
In order to maintain the qualification, the auditor should maintain knowledge of relevant requirements based on internal changes (ex, process technology, product technology) and external changes (ex, ISO 9001, IATF 16949, core tools, and customer specific requirements - Education for more than 4 hours per year. The auditor should execute at least 1 audits per year.)
Article 6 Attachments
QA-FO-19-01 Format Internal auditors
HSE System Audit Report
(Countermeasure Template) Permanent Quality Audit
(Report Template) OQA Core risk Q-Audit Report
(Report Template) Year 2025 Half Year Q-Audit Report
(Report Template) Year 2025 Monthly Q-Audit Report

## Slide 15
Article 7. Records retention policy
No. | Format No. | Format name | Champion | Time to keep | Way to keep
1 | - | Format Audit Plan | QA/CS | 5 years | Digital
2 | - | Format Program | QA/CS | 5 years | Digital
3 | - | Format Audit Report | QA/CS | 5 years | Digital
4 | - | Format CA Request | QA/CS | 5 years | Digital
5 | - | Internal audit list | QA/CS | 5 years | Digital
6 | - | Self Audit tool Year | QA/CS | 5 years | Digital
7 | - | (Countermeasure Template) Permanent Quality Audit | QA/CS | 5 years | Digital
8 | - | (Report Template) OQA Core risk Q-Audit Report | QA/CS | 5 years | Digital
9 | - | (Report Template) Year 2025 Half Year Q-Audit Report | QA/CS | 5 years | Digital
10 | - | (Report Template) Year 2025 Monthly Q-Audit Report | QA/CS | 5 years | Digital